# Key Dance = On - Off - On - Off - On within 5 seconds

11 
P0320 No Crankshaft Reference Signal At PCM 
P1390 Timing Belt Skipped Tooth 
P1391 Intermittent Loss Of CMP Or CKP 
P1398 Misfire Adaptive Numerator At Limit 

12 
Battery Disconnected 

13 
P1297 No Change In MAP From Start To Run 

14 
P0107 MAP Sensor Voltage Too Low 
P0108 MAP Sensor Voltage Too High 
P1496 5 Volt Supply Output Too Low 

15 
P0500 No VSS Signal 

16 
P0325 Knock Sensor Circuit 

17 
P1281 Engine Cold Too Long 
P0125 Closed Loop Temperature Not Reached 

21 
P0131 Upstream O2S Shorted To Ground 
P0132 Upstream O2S Shorted To Voltage 
P0133 Upstream O2S Slow Response 
P0134 Upstream O2S Stays At Center 
P0135 Upstream O2S Heater Failure 
P0137 Downstream O2S Shorted To Ground 
P0138 Downstream O2S Shorted To Voltage 
P0139 Downstream O2 Sensor Slow Response 
P0140 Downstream O2S Stays At Center 
P0141 Downstream O2S Heater Failure 

22 
P0117 ECT Sensor Voltage Too Low 
P0118 ECT Sensor Voltage Too High 

23 
P0112 IAT Sensor Voltage Low 
P0113 IAT Sensor Voltage High 

24 
P0121 TP Sensor Signal Does Not Agree With MAP 
P0122 TP Sensor Voltage Low 
P0123 TP Sensor Voltage High 

25 
P0505 IAC Motor Circuits 
P1294 Target Idle Not Reached (+/-200 RPM) 
P1299 Vacuum Leak Found (IAC Fully Seated) 

27 
P0201 Injector Circuit No. 1 
P0202 Injector Circuit No. 2 
P0203 Injector Circuit No. 3 
P0204 Injector Circuit No. 4 

31 
P0441 EVAP Purge Flow Monitor Failure 
P0442 EVAP Monitor Small Leak Detected 
P0443 EVAP Purge Solenoid Circuit 
P0455 EVAP Monitor Large Leak 
P1486 EVAP Monitor Pinched Hose Found 
P1494 Leak Detection Pump Switch Or Mechanical Fault 
P1495 Leak Detection Pump Solenoid Circuit 

32 
P0401 EGR System Failure 
P0403 EGR Solenoid Circuit 

33 
P0645 A/C Clutch Relay Circuit 

34 
P1595 Speed Control Solenoid Circuit 
P1596 Speed Control Switch Always High 
P1597 Speed Control Switch Always Low 

35 
P1491 Radiator Fan Control Relay Circuit 

37 
P0740 TCC No RPM Drop At Lockup 
P0743 TCC Solenoid Circuits 
P1899 P/N Switch Stuck In Park or Gear 

41 
P0622 Generator Field Improper Switching 

42 
P1282 Fuel Pump Relay Control Circuit 
P1388 ASD Relay Control Circuit 
P1389 No ASD Relay Output Voltage At PCM 
P0460 Fuel Level Sending Unit & Circuit, No Change Over Miles 
P0462 Fuel Level Sending Unit Voltage Out Of Limits, Too Low 
P0463 Fuel Level Sending Unit Voltage Out Of Limits, Too High 

43 
P0300 Multiple Cylinder Misfire 
P0301 Misfire Cylinder No. 1 
P0302 Misfire Cylinder No. 2 
P0303 Misfire Cylinder No. 3 
P0304 Misfire Cylinder No. 4 
P0351 Ignition Coil No. 1 Primary Circuit 
P0352 Ignition Coil No. 2 Primary Circuit 

44 
P1492 Ambient/Battery Temperature Sensor Voltage High 
P1493 Ambient/Battery Temperature Sensor Voltage Low 

46 
P1594 Charging System Voltage Too High 

47 
P1682 Charging System Voltage Too Low 

51 
P0171 Fuel System Lean 

52 
P0172 Fuel System Rich 

53 
P0600 PCM Failure SPI Communications 
P0601 Internal Controller Failure 

54 
P0340 No Cam Signal At PCM 

55 
DTC Fault Display Complete 

61 
P0106 Barometric Pressure Out Of Range 

62 
P1697 PCM Failure SRI Mile Not Stored 

63 
P1696 PCM Failure EEPROM Write Denied 

65 
P0551 PS Pressure Switch Failure 
P0703 Brake Switch Stuck, Pressed, Or Released 

71 
P1496 5 Volts Output From Regulator Low 

72 
P0420 Catalyst Efficiency Below Required Level

77 
P1683 Speed Control Power Relay Circuit